## Slide 1: Specialist Extension Level Secondary Food Health and Safety (SFHS)
The Design and Technology Association
Jeff Knox RDTHSC 0546

## Slide 2
BS4163 - 2014
Health and safety for design and technology in educational and similar establishments. Code of practice.

## Slide 3: What is required for SFHS certificate?
SFHS Standards:
Level 2 Certificate in Food Hygiene.
Fixed equipment and the environment certificate.
Small portable equipment certificate.
Temperature control, contamination and
allergies certificate.

## Slide 4: Fixed equipment and the environment
  Hazards and control measures: electric shock, gas, hot surfaces and steam, bacterial growth, entanglement, flooring, lighting,
  Practical skills: Evidence: risk assessment in SOW, students written training record, maintenance records, cleaning schedules

## Slide 5
A modern food room layout

## Slide 6
A more traditional
food room layout

## Slide 7
Another more traditional
food room layout

## Slide 8
A refurbished
food room layout

## Slide 9
Fixed Equipment

## Slide 10: Drinking water in a food room
Taps should be labelled

## Slide 11
Risk Assessment
Model Risk assessments are based on:
Health and Safety Training Standards in
Design & Technology 2017
BS4163:2014 BRITISH STANDARD Health and
safety for design and technology in schools and
similar establishments
Model Risk Assessments for design and technology:
CLEAPSS

## Slide 12
‘ADOPT AND ADAPT’
Points to consider:
The activity
Skills/ experience / training
Level of supervision / support required
Any restrictions
Any room layout/space/circulation problems
Maintenance of equipment/appliances/machinery/tools
Any training/accreditation required

## Slide 13: Training students in risk assessment. When and how?
Training records?

## Slide 14: Teaching and Learning Strategies
How are H&S issues incorporated into your schemes of work?
How is H&S training provided for learners?
How this training is recorded?

## Slide 15
Task 1.
Writing a Risk Assessment.
By adapting and adopting the model risk assessment complete a risk assessment for your school.
http://www.cleapss.org.uk/secondary/secondary-dandt/secondary-dant-model-risk-assements

## Slide 16: Why maintenance is important?
Meet all current legislation, insurance requirements and responsibilities
  Control of substances Hazardous to Health (COSHH) 2002 Regulations,
  Provision and Use of Work Equipment Regulations (PUWER) 1998,
  Lifting Operations and Lifting Equipment Regulations (LOLER) 1998
  BS4163:2014 Health and safety for design and technology in educational and similar establishments - Code of practice.
  BS7671:2008 Wiring regulations
  HSE Guidelines HSG 258 - Controlling airborne contaminants at work
Ensure equipment is safe for you and your students.
Carrying out Portable Appliance Testing within the suggested 12 month intervals. (Or at other previously agreed intervals depending on use).
Extend the working life of your equipment .

## Slide 17: Portable Appliance Testing (PAT)
Portable Appliance Testing
Carried out regularly on equipment in your material work area, or one that you regularly work in. An appropriate label is evidence.

## Slide 18
Cleaning – Keeping food safe
Food preparation areas must be kept clean to protect from:
microbial contamination – reduce bacteria to a safe level, reduce cross contamination.
physical contamination – removing objects that could
fall into food.
chemical contamination – washing away pesticide
residue and chemical cleaning residue

## Slide 19: When to clean?
Best practice – Clean as you go.
Prevent build up of dirt and waste.
Before disinfection
Food contact surfaces should be cleaned before commencing work and immediately after.
If you made the mess then you should clean it up!
Lower risk areas such as floors, should be cleaned at the end of the day.
Specialist cleaning as required e.g. tiles around sink areas, extractor fans

## Slide 20: Cleaning Materials
Storage and use of cleaning materials.

## Slide 21: COSHH Data Sheets

## Slide 22
Cleaning Schedule

## Slide 23: Cleaning Schedules
What, when by whom, with what, how and PPE needed.

## Slide 24
Workplace (Ventilation and heating) | Does the room have natural ventilation
 | Can a reasonable room temperature be maintained during use of the classroom
 | Are measures in place, for example blinds to protect from the glare and heat of the sun
Health and Safety Executive checklist for classrooms
Ventilation and Heating
This is particularly important if you are storing pupil ingredients and made dishes at room temperature. If it was proved that you knew about the high temperature and there was an incident in your classroom (pupil passing out with heat and injuring themselves, or got food poisoning as dish was stored incorrectly) you would be personally liable in a court of law, until you have asked your school to investigate this issue. Once it is known to the head teacher, it is then their responsibility as the employer to secure your Heath & Safety.
World Health Organization says that, in temperate climates, the optimum indoor temperature is between 18°C and 24°C.
Implications for food
activities in relation to the
Danger Zone

## Slide 25: Small portable equipment
.
  Hazards and control measures. Shock, tripping, rotating blades, cutters, sharps blades, hot substances, inadvertent starting, fire hazard fat fryers, high pressures overheating, entrapment, flooring, lighting.
  Practical skills: demonstrate the safe use of: knives and peelers, processors, hand held blender microwave oven, pressure cooker, deep fat fryer

## Slide 26: Task 2
Demonstrating safe use of equipment.

## Slide 27
Discuss
Look for the Hazards?
Look at the images
Who might use these items?
What might they use them for?
Share ‘near miss’ events
Review existing control measures
Think about control measures?
What precautions could be taken when using these items?
Think about safer alternatives?
Where can you find suggested control measures?

## Slide 28
How do you store your knives?
In a tray like this??
How many knives should there be?
How many are there?
How long does it take to count them in?
If the first student is withdrawing a knife while the second student is going in to pick up another. The result can easily be cuts to the hand.
Think about control measures
Why not use knife blocks similar to this?
No need to count knives in – just spot the gap
All sharp edges are enclosed while stored
Access to the knife is only via the handle

## Slide 29
Risk Assessment Discussion Hazards and Control Measures
Hazard
Anything that could cause harm, or have potential to hurt or cause damage
Control Measure
Reduce risk
Reduce likelihood of harm
Limit possibility of harm
Suggest safer alternative
Remember: Risk Assessment is the key
Evidence of training, demonstration, support for learner, signage, reminders

## Slide 30
A
B
C

## Slide 31
Should this equipment be used at KS3/GCSE or is it just for Catering courses?

## Slide 32
Do you discuss the relative dangers of ring pull and can opener types?

## Slide 33
The law requires that food equipment must:
Be kept clean and in good condition
Enable thorough cleaning and disinfection
Be installed to allow cleaning of the surrounding area
Minimise the risk of contamination.

## Slide 34: Temperature control contamination and allergies
  Hazards and control measures. Purchase, dry and cold storage, preparation, cooking, cooling, reheating, hot holding serving and sale of foods, materials and components that could be injurious to health.
  Practical skills: Evidence: system to monitor temperatures fridge freezer, cleaning schedule, display materials in classroom.

## Slide 35: Chilled Storage - Fridges
• clean and defrost thoroughly
• cover and label food
• keep food tidy
• don’t over stock
• FIFO
• no warm food
• separate raw and ready-to-eat foods
• decant food from metal containers
consider labelling fridges uncooked foods and cooked foods
If students bring their own ingredients, is a domestic
Refrigerator suitable for cooling 40 to 60 small containers of
High risk food that has warmed to room temperature during
The trip from home to school?

## Slide 36: Storage of high risk foods in school
How do you monitor the actual temperature in your fridges? A loose thermometer (Theft) or self adhesive thermochromic labels? (Permanent, unbreakable & battery free).

## Slide 37: Frozen Storage
• clean and defrost thoroughly (if not frost free)
• cover and label food
Include the date
• keep food tidy
• don’t over stock
• no warm food
• FIFO

## Slide 38: Chopping Boards

## Slide 39: Allergens - 14

## Slide 40: Allergens

## Slide 41: Allergens If an allergic reaction is going to happen in a school it will almost certainly be in the dining area or the food room. The student may have forgotten to bring their epi-pen. Where does your school keep the spares? The school office? The first aid room? Not a good idea! Why can you not be trusted to keep it under lock and key in the food room? Epi-pens cannot kill and you are already trusted with a lot of sharp knives.

## Slide 42: Ingredients in schools
Does school provide all or some of the ingredients?
Does school provide the odd ingredient e.g. eggs, flour, spices, flavouring

## Slide 43: Safety in Food Technology
Looking at Time and Temperature control:
Individual ingredients/dish - controls
Shopping
Day before
Storage on way to school
Storage at school
Lesson start
Preparation
Start of 60 min lesson
Cooking
Mid-end of 60 minute lesson
Chilling and packaging
End of 60minute lesson
Storage and labelling
End of lesson to end of school day
Transporting home
End of school until product consumed
Reheating – and eating 7pm
Time
Temperature control

## Slide 44: Task A Day the Life of a Shepherds Pie’
Hazards Analysis and Critical Control Points (HACCP)
From the purchase of the ingredients to make the pie……
…..to the eating of the finished pie.

## Slide 45: Dry Storage in Schools
How do you store dry goods?
Flour, sugar, spices, flavourings etc.
Best before dates??

## Slide 46: Use by and best before ….

## Slide 47: Eggs - Best before date.

## Slide 48: Checking Food is Cooked.
Meat/Chicken products -
Visual checks
Temperature probes checks.

## Slide 49: Reheating food prepared at school.
Instructions for reheating?

## Slide 50: Task
4a Set up a safe taste test.
4b Prepare the Risk Assessment for the activity.